## Slide 1
Cement:
Cement is the mixture of calcareous, siliceous, argillaceous and other substances. Cement is used as a binding material in mortar, concrete, etc.

## Slide 2: Chemical Composition of cement is:
Lime | 63%
Silica | 22%
Alumina | 06%
Iron oxide | 03%
Gypsum | 01 to 04%

## Slide 3: Bogue’s Compounds C3S & C2S PRVIDE STRENTH & OFFERS RESISTANCE TOWARDS THE
A
TTACK OF ACIDS & ALKALIES.
Name of Compound | Formula | Abbreviated Formula
Tricalcium silicate | 3 CaO.SiO2 | C3S –hydrates rapidly;
 |  | provides early & ultimate
 |  | strength
Dicalcium silicate | 2 CaO.SiO2 | C2S-hydraes slowly&
 |  | provides strength after a
 |  | duration of 7 days
Tricalcium aluminate | 3 CaO.Al2O3 | C3A-hydrates rapidly;
 |  | provides early strength &
 |  | less ultimate strength
Tetracalcium aluminoferrite | 4 CaO.Al2O3.Fe2O3 | C4AF-doesn’t provide
 |  | strength but is stable than
 |  | C3A

## Slide 4: TYPES OF CEMENT:
15. White Cement
Ordinary Portland Cement
Rapid Hardening Cement (or) High Early Strength cement
Extra Rapid Hardening Cement
Sulphate Resisting Cement
Quick Setting Cement
Low Heat Cement
Portland Pozzolana Cement
Portland Slag Cement
High Alumina Cement
Air Entraining Cement
Supersulphated Cement
Masonry Cement
Expansive Cement
Colored Cement

## Slide 5: (1) ORDINARY PORTLAND CEMENT:
It is called Portland cement because on hardening (setting) its colour resembles to rocks near Portland in England. It was first of all introduced in 1824 by Joseph Asp din, England.
Most important type
Classified into three grades, namely 33 grade, 43 grade and 53 grade.

## Slide 6: Chemical Composition of O.P.Cement:
O.P.C has the following approximate chemical composition:
The major constituents are:
1. Lime | (CaO) | 60- 63%
2. Silica | (SiO2) | 17- 25%
3. Alumina | (Al2O3) | 03- 08%

## Slide 7: Chemical Composition of O.P.Cement: Continued-------
The auxiliary constituents are:
1. Iron oxide (Fe2O3) | 0.5- 06%
2. Magnesia (MgO) | 1.5- 03%
3. Sulphur Tri Oxide (SO3) | 01- 02%
4. Gypsum | 01 to 04%

## Slide 8: Functions of Cement Manufacturing Constituents

## Slide 9: (i) Lime (CaO):
Lime forms nearly two-third (2/3) of the cement. Therefore sufficient quantity of the lime must be in the raw materials for the manufacturing of cement.
Its proportion has an important effect on the cement. Sufficient quantity of lime forms di- calcium silicate and tri-calcium silicate in the manufacturing of cement.
Lime in excess, causes the cement to expand and disintegrate.

## Slide 10: (ii) Silica (SiO2):
The quantity of silica should be enough to form di-calcium silicate and tri-calcium silicate in the manufacturing of cement.
Silica gives strength to the cement.
Silica in excess causes the cement to set slowly.

## Slide 11: (iii) Alumina (Al2O3):
Alumina supports to set quickly to the cement.
Lowers the clinkering temperature.
Alumina in excess, reduces the strength of the cement.

## Slide 12
(iv) Iron Oxide (Fe2O3):
Iron oxide gives colour to the cement.

## Slide 13
(v) Magnesia (MgO):
It also helps in giving colour to the cement.
Magnesium in excess makes the cement unsound.

## Slide 14
(vi) Calcium Sulphate (or) Gypsum (Ca SO4) :
At the final stage of manufacturing, gypsum is added to increase the setting of cement.

## Slide 15: (2) RAPID HARDENING CEMENT:
Also known as early gain in strength of cement. This cement contains more %age of C3S and less %age of C2S, high proportion of C3S will impart quicker hydration
The high strength at early stage is due to finer grinding, as fineness of cement will expose greater surface area for the action of water.
The strength obtained by this cement in 03 days is same as obtained by O.P.C in 7 days.
Initial and final setting times are same as OPC.ie. 30mins and 10 hrs.And soundness test by Le-Chatielier is 10mm and Autoclave is 0.8%.
Greater lime content than OPC

## Slide 16
(3) EXTRA RAPID HARDENING CEMENT:
It is obtained by intergrinding Cacl2 with rapid hardening cement.
Addition of Cacl2 should not exceed 2% by weight of the rapid hardening cement.
Concrete made by using this cement should be transported, placed, compacted & finished within about 20 minutes.
Strength is higher than 25% than that of rapid hardening cement at 1 or 2 days.

## Slide 17
(4) SULPHATE RESISTING CEMENT:
It is modified form of O.P.C and is specially manufactured to resist the sulphates.
This cement contains a low %age of C3A and high
%age of C3S
This cement requires longer period of curing.
It develops strength slowly, but ultimately it is as strong as O.P.C.

## Slide 18: (5) QUICK SETTING CEMENT:
This cement is manufactured by adding small
%age of aluminum sulphate (Al2SO4) which accelerates the setting action.
Gypsum content is reduced.
Sets faster than OPC.
Initial setting time is 5 minutes. Final setting time is 30 minutes.

## Slide 19: (6) LOW HEAT CEMENT:
Low percentage of tri-calcium aluminates (C3A) and silicate (C3S) and high %age of di-calcium silicate (C2S) to keep heat generation low.
Very slow rate of developing strength as rate of C3S Content is low.
Heat evolved @ 7 days-66 cal/g and 28 days-75 cal/g
initial set time-1 hr, final set time-10 hrs
Better resistance to chemical attack than OPC.

## Slide 20: (7) Portland Pozzolana Cement:
OPC clinker and Pozzolana (Calcined Clay, Surkhi and Fly ash) ground together.
Produces less heat of hydration and offers great resistance to attacks of Sulphates.
Used in marine works and mass concreting.
Ultimate strength is more than OPC.
Low shrinkage on drying
Water tightness.

## Slide 21: (8) Portland Slag Cement:
Produced by mixing Portland cement clinker, gypsum and granulated blast furnace slag which shall not exceed 65%
blackish grey in color.
Lesser heat of hydration.
Suitable for marine works, mass concreting.
Offers good resistance to the attack of sulphate.

## Slide 22: (9) HIGH ALUMINA CEMENT:
Different from OPC
Characterised by its dark colour, high heat of hydration and resistance to chemical attack.
Initial setting time of 4 hrs and final setting time of 5 hrs.
Raw materials used are limestone and bauxite

## Slide 23: (10) AIR ENTRAINING CEMENT:
OPC with small quantity of air entraining materials (oils, fats, fatty acids) ground together.
Air is entrained in the form of tiny air bubbles which enhances workability and reduces seggregation and bleeding.
It increases sulphate water resistance of concrete.

## Slide 24: (11) Supersulphated Cement:
Ground blast furnace slag + OPC +CASO4. Heat of hydration which is considerably lower.
•
•
It is also resistant to Sulphate attack.
Used in a) Marine Structures, b) Mass concrete works

## Slide 25: (12) Masonry Cement:
Unlike ordinary cement, it is more plastic.
Made by mixing hydrated lime, crushed stone, granulated slag or highly colloidal clays are mixed with it.
Addition of above mentioned materials reduces the strength of cement.

## Slide 26: (13) Expansive Cement:
The main difference in this cement is the increase in volume that occurs when it settles.
Used to neutralize shrinkage of concrete made from ordinary cement so as to eliminate cracks. A small percentage of this cement with concrete will not let it crack. It is specially desirable for hydraulic structures.
In repair work, it is essential that the new concrete should be tight fitting in the old concrete. This can be done by using this cement

## Slide 27: (14) Colored Cement:
Suitable pigments used to impart desired color.
Pigments used should be durable under light, sun or weather.

## Slide 28: (15) WHITE CEMENT:
OPC with pure white color produced with white chalk or clay free from iron oxide.
As iron oxide gives the grey colour to cement, it is therefore necessary for white cement to keep the content of iron oxide as low as possible.
Instead of coal, oil fuel is used for burning.

## Slide 29: THE PLEASANT END